## Slide 1: Simulation of production process-related adhesive damage of the adhesively bonded multi-material body in white
Suba Siva Chandran Kalimuthu
Matrikel nr: 4868941

## Slide 2: Overview
Mechanical simulation material properties
Other aspects of Mechanical simulation

## Slide 3: Mechanical simulation material properties
Units used:
Young’s modulus – N/mm2
Material properties | Steel | Aluminium | Spotwelds
Young’s modulus | 210000 | 69000 | 210000
Poisson ratio | 0.3 | 0.3 | --
Thermal expansion | 1.3e-5 | 2.4e-5 | 4e-4

## Slide 4: Mechanical simulation material properties
Adhesive:
Same material properties which have been provided by Mr.Günther, based on the Damage by Traction separation law. I have attached that in a word document in the same folder
In addition, I have specified the Thermal expansion for the Adhesive based on temperature
Thermal expansion coeff | Temperature(°C)
0.000228 | 23
0.0003 | 115
0.000365 | 160
0.0004 | 180

## Slide 5: Other aspects of Mechanical simulation
Step
Simulation Time period – 2400 seconds
Load
  Temperature field obtained as a result from the Thermal simulation
    Mesh
    Steel and Aluminium – Shell elements (S4 and S3)
    Spot welds – Solid elements (C3D8)
    Adhesive – Cohesive elements (COH3D8)