## Slide 1: Simulation of production process-related adhesive damage of the adhesively bonded multi-material body in white
Suba Siva Chandran Kalimuthu
Matrikel nr: 4868941

## Slide 2: Overview
Transient Thermal simulation material properties
Steel Hat profile
Aluminium Plate
Finalized film coefficient for Thermal simulation
Other aspects of Transient Thermal simulation

## Slide 3: Transient Thermal simulation material properties
Units used:
Density – ton/mm3 Thermal conductivity – mW/mmK
Specific Heat capacity – mJ/tonK
Material properties | Steel | Aluminium | Adhesive | Spotwelds
Density | 7.85e-009 | 2.71e-009 | 1.2e-009 | 7.85e-009
Thermal conductivity | 52 | 237 | 2 | 52
Specific heat | 0.48e9 | 0.91e9 | 12e8 | 0.48e9

## Slide 4: Transient Thermal simulation material properties
Steel Hat profile:
Simulation_1 | Simulation_2 | Simulation_3 | Temperature (°C)
0.003 | 0.005 | 0.006 | 20
0.008 | 0.009 | 0.008 | 80
0.012 | 0.012 | 0.012 | 140
Simulation Attempt | Room Temperature(°C)
Simulation_1 | 23
Simulation_2 | 20.5
Simulation_3 | 18

## Slide 5: Transient Thermal simulation material properties
Aluminium plate:
For Aluminium, we have done one experiment and I have used the above film coefficients to fit that experimental data
Film coefficient (mW/mm2K) | Temperature (°C)
0.008 | 20
0.023 | 80

## Slide 6: Finalized Film coefficient for Thermal simulation
Steel:
Aluminium:
Room Temperature: 20.5°C

## Slide 7: Other aspects of Transient Thermal simulation
Step
Simulation Time period – 2400 seconds
Load or Thermal Boundary condition
    Predefined field Temperature – 180°C on entire BIW
    Mesh
    Steel and Aluminium – Heat transfer elements (DS4 and DS3)
    Spot welds & Adhesive – Solid Heat transfer elements (DC3D8)